## Slide 1: 2.2 Mechanical science principles PowerPoint 2: Mechanical science principles
2. Construction science principles

## Slide 2: Energy

## Slide 3: Energy
Energy is used to heat, power and light our built environment.
In science, energy is expressed as the amount of work done by a force.
Energy cannot be created or destroyed, only converted from one form to another.
The units of energy are joules (J).
A transducer is a device that converts energy from one form to another. For example, a 12V car battery is a transducer which converts chemical energy into an electromotive force of 12V.

## Slide 4: Energy
Energy can be either kinetic or potential.
Kinetic energy is energy due to motion, for example a car accelerating.
Potential energy is stored energy that depends on relative position within a system. For example, a raised weight, a car parked at the top of a slope, or a pulley.

## Slide 5: Force
A force is defined as a push or pull that changes an object’s state of motion or causes the object to deform.
There are four fundamental forces in nature:
gravity – a force which attracts items that have mass or energy
electromagnetism – the interaction of particles with an electrical charge
weak interaction and strong interaction – these happen at an atomic level (inside atoms).

## Slide 6: Force
Forces act on structures in a number of different ways:
gravity pulling downwards
self weight
imposed loads
live loads.
Notes: For more see: https://www.nasa.gov/audience/forstudents/k-4/dictionary/Force.html

## Slide 7: Force
The SI unit of force is the newton (N).
A newton is the amount of force required to give a 1kg mass an acceleration of 1m/s/s.
A force has both magnitude (how much) and direction (the direction it is applied in).
In order for a structure to be in equilibrium all forces need to be in balance.
If imbalance occurs, then structural elements will settle and deflect, causing aesthetic and structural damage. You may not be able to see a force, but you can see its effects.
Gravity at work: falling debris
Notes: Suggest explaining both scalar and phasor quantities.
Then basic calculations explaining Newton’s second law.

## Slide 8: Tension, compression and shear forces
Compression is the force generated from compressing an object, eg the force at work in compression brakes or hand tools.
Tension: ‘tensile force’ describes the stretching forces acting on a material, eg the force at work in the cables of a suspension bridge.
Shear force is that applied perpendicular to a surface, as opposed to an offset force. One part of the surface is pushed in one direction, while another is pushed in the opposite direction. Engineers and architects consider shear forces when building high-rise structures to resist wind and seismic forces.

## Slide 9: Work
The amount of work done is expressed as the amount of effort put into a mechanical principle. For example, we need to know how much work an electrical motor can produce to match it with the process requirements.
Work done = force x distance
Notes: http://hyperphysics.phy-astr.gsu.edu/hbase/work2.html

## Slide 10: Work
In the calculation:
Work done = force x distance
work done is measured in joules (J)
force is measured in newtons (N)
distance moved is measured in metres (m)
1 joule of work is done when a force of 1 newton causes a movement of 1 metre. This means that work done can be measured in newton metres (Nm) as well as in joules.

## Slide 11: Work: an example
Assume a person weighs 650N. A lift needs to move the person 50m to the top floor of a building.
How much work is done?
Work done = force x distance
Work done = 650N x 50m
Work done = 32,500J (or 32.5kJ)

## Slide 12: Power
Power is often specified in construction as any of the following.
The amount of power in watts (W) required – eg for a lift motor.
The amount of power in volts (V) – eg a single- or three-phase electrical supply.
The amount of horsepower (hp) – eg that delivered by a diesel engine in an excavator.
Power is a measure of the rate of energy which is delivered to a process.
Power = the amount of energy transferred per second

## Slide 13: Expressing power
This can be expressed as
Power (P) is measured in watts (W)
Work done (E) is measured in joules (J)
Time (t) is measured in seconds (s)
A heater uses 48,000J of energy in 1 minute.
What is the power rating of the heater?
The heater has a power rating of 800W.
Notes: For more revision of this topic see: Power - Power and efficiency - Edexcel - GCSE Physics (Single Science) Revision - Edexcel - BBC Bitesize

## Slide 14: Efficiency
How well a device transfers energy input into useful energy output is called efficiency.
A very efficient device wastes very little of the energy which is put into it.
Efficiency =
Efficiency is usually expressed as a percentage (by multiplying by 100).
Inefficient devices will waste a large proportion of their input energy. For example, filament lightbulbs are inefficient as only a small proportion of their input energy is transferred into light (useful energy).
The efficiency of a photovoltaic cell in converting sunlight to electrical energy is around 20%. Large areas of solar cells are required to generate useful amounts of electricity.
Notes: For revision on efficiency see: Efficiency - Power and efficiency - Edexcel - GCSE Physics (Single Science) Revision - Edexcel - BBC Bitesize

## Slide 15: Velocity
The velocity of an object is expressed as:
Velocity (V) =
For example, a car travels 300m in 120s: what is its velocity?
V =
V = 2.5 m/s

## Slide 16: The theory of moments
A basic concept of mechanics is the theory of moments. The turning effect of a force is known as the moment. A moment is a force expressed as a bending over the distance applied.

## Slide 17: Theory of moments
Moment of force (Nm) = force (N) x perpendicular distance from the force to the pivot (m).
Example
It is easier to undo a tight nut with spanner, rather than by using your fingers. This is because the handle of the spanner increases the distance away from the pivot, meaning less force is required to create the moment (turn).

## Slide 18: Force (action) and reaction

## Slide 19: Tension, compression, shear and bending
Compression occurs in the top of the beam
Reaction left
Reaction right
Force
The beam bends with the distance of the force from the end
Shear occurs at the ends of the beam
Tension occurs in the bottom of the beam

## Slide 20: Centre of gravity
To prevent an object overturning, it is often necessary to know its centre of gravity.
The centre of gravity of standard shapes can be found by drawing the middle point via the lines of symmetry. In the illustration, the centre of gravity is where the two red lines cross.

## Slide 21: Equilibrium
When in equilibrium, the total sum of the anticlockwise moment is equal to the total sum of the clockwise moment.
When a system is stable or in balance it is said to be in equilibrium as all the forces acting on the system cancel each other out.
Person A is twice as heavy as person B, so must sit half the distance away (1m) from the pivot or fulcrum than person B sits (2m) to be in equilibrium.

## Slide 22: Mechanical advantage
Mechanical advantage is the effectiveness of a simple machine (such as a lever, a wheel and axle or a pulley system) to amplify a force.
The mechanical advantage of a system is the ratio of the force that performs the useful work to the force applied.
For example, levers operate with mechanical advantage. This means that the lever can overcome a large load with relatively little effort.
Notes: For a video on this see: Block and Tackle (Pulley, Work, Mechanical Advantage, Machine) | Physics | CK-12 Exploration Series (ck12.org)

## Slide 23: Levers
A lever allows an extension of force to be exerted.
For example, a spade has a long handle so it can be levered back when excavating a cable trench.

## Slide 24: Pulleys
A pulley is a mechanical component that is used with cables and allows a greater force to be exerted. It is a simple machine used to lift weights. The object being moved is known as the load. Pulleys are assembled to form a block and tackle in order to provide mechanical advantage to apply large forces. It consists of a cable which is attached to a wheel and axle. For example, a drag line uses pulleys and cables to excavate large amounts of earth.

## Slide 25: Fixed, moveable and ‘gun tackle’ pulleys

## Slide 26
Any questions?