## Slide 1: PowerPoint 3: Electricity principles
PowerPoint presentation
2. Construction science principles
2.3 Electricity principles

## Slide 2: Sources of power
Fossil fuels – oil, gas and coal.
Nuclear power – a controversial fuel, especially since radioactivity remains active for hundreds of years.
Renewable energy – solar, wind, water.

## Slide 3: How power is generated from fuel
Coal – coal-fired power stations burn coal to turn water into steam which drives a turbine (electrical generator).
Oil and gas – these fossil fuels produce heat on burning which generates electricity.
Nuclear power – relies on fusion to produce heat, then steam, etc.
Renewable generation – eg wind farms producing ‘clean’ energy by turning a turbine using the power of the wind.
Hinkley Point C is a new nuclear power station, shown here under construction in 2021.

## Slide 4: Components of a power generation system

## Slide 5: Distribution
The UK has a ‘super grid’ to distribute high voltages nationally, called the National Grid.
Before electrical power leaves a power station it is transferred at high voltages by using ‘step-up’ transformers to increase the voltage to around 275,000V. Pylons are mainly used within the UK to distribute power over distances.
Before electrical power enters homes and factories the voltages are decreased by ‘step-down’ transformers.

## Slide 6: Units of measurement for electricity
The base SI unit of amperes (A) is the unit of measurement for current. For example, lighting circuits don’t need as much energy and are 5A, whereas power circuits require 13A.
A volt (V) is the derived unit for electric potential, electric potential difference (voltage) and electromotive force.
The ohm (Ω) is the derived unit of electrical resistance.
The watt (W) is the SI unit of power, used to measure the rate of energy transfer.

## Slide 7: Electromagnetic induction
When rotated around each other, a magnet and a copper coil of wire create an electrical force.
A voltage is produced when a magnet moves into a coil of wire. This process is called electromagnetic induction. The direction of the induced voltage is reversed when the magnet is moved out of the coil again. If the coil is part of a complete circuit then a current will be induced in the circuit.
This principle is what an electrical generator consists of: a copper coil surrounded by a magnet which generates electricity.
Notes: Electricity and magnetism are symbiotic, in other words you cannot have one without the other.
Therefore, when a conductor is moved through a magnetic field it creates an electromagnetic force, and this is known as the generator principle.
For more see: Electromagnetic induction - Electromagnets and motors - GCSE Physics (Single Science) Revision - BBC Bitesize

## Slide 8: Resistance
All conductors show some opposition to electrical current. This opposition to current is called resistance. There are several factors that affect the resistance of a conductor such as:
material – copper is a better conductor than steel as it has a lower resistance
thickness – wires with smaller diameters have greater resistance
length – the longer the wire, the greater the resistance
temperature – heating a wire increases its resistance.
The two main ways of increasing the current in an electrical circuit are by increasing the voltage or by decreasing the resistance.

## Slide 9: Voltage, currents and resistance
Power remains unchanged within a transformer, therefore when voltage is boosted to very high levels, the output current is reduced significantly.
Heat and the amount of voltage dropped across the conductors are also significantly reduced.
Thereafter, smaller conductors can be used in the transmission of electricity.
This means transformers ensure that the transmission of electricity is as efficient as possible.

## Slide 10: Transformers
There are various types of transformer: step-up and step-down (power transformers), which can be either three-phase or single-phase. In addition there are:
current transformers (eg clamp meters)
safety isolation transformers (eg electric shavers)
autotransformers (reduced voltage systems such as a 110V supply)
differing equipment supplies, eg 12V (battery), 230V (mains).
Industrial equipment cannot necessarily run on 12V, 110V or 230V because there is insufficient power (current) to drive heavy loads. Therefore, three-phase 400V supplies are used for larger electrical motors.

## Slide 11: Step-up and step-down transformers
Step-up and step-down transformers allow us to easily multiply or divide voltage and current in AC circuits. AC voltage can be ‘stepped up’ and current ‘stepped down’ for reduced wire resistance power losses along power lines.
Notes: Tutor notes Suggest you stipulate that there is no electrical link between the Primary (input) and the Secondary (output), which is why transformers are used as Safety Isolation devices. Equally that magnetic link needs to be continually pulsed, which is why transformers only work with alternating current.

## Slide 12: Three-phase transformers
Three-phase transformers are static electromagnetic devices made to transmit energy or send alternating electrical signals between circuits. This equipment is mainly used for industrial purposes to generate, transmit and distribute electrical energy.

## Slide 13: Electricity in the built environment
Domestic properties do not normally need more than 100A to supply their electrical loads and a 230V single-phase supply can provide this.
A large factory or commercial premises (eg a hotel or school) will need far more than 100A, and will therefore have a 400V, three-phase & neutral supply.
In construction, 110V is used onsite, because it is a safer voltage. This is known as a reduced voltage system.

## Slide 14
Any questions?