## Slide 1: PowerPoint 5: Heat principles
PowerPoint presentation
2.Construction science principles
2.5 Heat principles

## Slide 2: Heat transfer and loss
Heat transfer refers to conduction, convection and radiation. How they are managed within a building will have a direct effect on that building’s ‘environmental footprint’.
Heat loss in a building is affected by the fabric, the extent and type of ventilation and the internal air temperature.

## Slide 3: Conduction
Conduction refers to heat moving through a material or from one material to another via direct contact.
The heat is transported as atoms vibrate with kinetic energy.
Some materials (eg metals) conduct efficiently, whereas non-metals and gases are poor conductors.

## Slide 4: Convection
Heat energy is transferred from hot places to cooler places by convection.
Convection occurs when particles with a lot of heat energy in a liquid or gas move and take the place of particles with less heat energy.

## Slide 5: Radiation
Unlike conduction and convection, which require particles in a solid, liquid or gas, infrared radiation is a type of electromagnetic radiation that involves waves.
The sun is 150 million km away, but we still experience its heating effects via radiation.

## Slide 6: Reducing heat transfer in buildings
Heat is lost from homes by:
conduction through the walls, floor, roof and windows
convection – when cold air enters through doors and window gaps, convection currents transfer heat energy to the loft/roof
radiation through the walls, roof and windows.
Carpets, curtains and double glazing all reduce heat loss.
Cavity wall insulation prevents air circulating in the cavity.
Roof insulation also reduces heat loss through the roof.
Notes: For more see: Measures to help reduce home heat loss - Energy Saving Trust

## Slide 7: Characteristics of air: temperature, density and humidity
Temperature: in the UK we have to design heating systems for a range of temperatures from -1 to 21 degrees Celsius.
Density: air has density – the higher up you go in the atmosphere the less dense air becomes.
Humidity: air contains water vapour which is measured as a percentage (%) in terms of humidity.

## Slide 8: Condensation
Condensation occurs when hot, humid air touches a colder surface. For example, a kettle’s steam landing on a cold window surface produces droplets of moisture.
Condensation can occur as a surface feature or interstitially, eg inside a material such as a brick or block of a cavity wall.
Condensation occurs in poorly heated, poorly ventilated and poorly insulated buildings. The damp produced by condensation encourages mould, which can be the cause of health problems.

## Slide 9: Reducing condensation
Modern building design reduces condensation through a variety of methods.
Increased levels of cavity insulation (150mm wide).
Reduction in air leakage from the building.
Background ventilation (the flow of air into a building without the need to open a window).
Ventilation at source – eg extractors over cookers, fans in bathrooms.

## Slide 10: Effects of moisture on construction materials
Timber – when timber becomes damp due to condensation over time, this can result in the timber starting to break down and rot. The wood then loses its structural integrity.
Plaster – wet plaster becomes mouldy and deteriorates.
Steel – rust (corrosion) develops over time.
Paintwork – fungal spores have to be treated and wiped off paintwork which may require recoating.
Moisture can also cause corrosion within electrical components and wiring, which must then be replaced.

## Slide 11: Thermal conductivity: R-, K- and U-values
The U value is the total thermal resistance of a building, expressed as 1/Rt. This produces a value which must meet Part L of the approved documents for building regulations. U-values are always measured in W/m2K (watts per metre squared kelvin).
The R-value is a measure of the thermal resistance of a material. The higher the R-value, the greater the insulating power.
The R-value is calculated by dividing the thickness of a material in metres by its K-value (its thermal conductivity). R-value information is available when selecting suitable insulation.

## Slide 12: Thermal conductivity calculations
Resistance (R)
Resistance is calculated as R =
T is the thickness in metres, K relates to thermal conductivity (the ‘K factor’).
Thus to calculate the resistance (U) of a standard brick if its K-value is 0.84 we divide its thickness by its thermal conductivity, in this case 0.100 ÷ 0.84, giving us 0.11.

## Slide 13: Effects of thermal expansion
All materials expand and contract due to changes in temperature. If this is not allowed for in building design, then cracking can occur.
For example, every 6m in a brick wall there has to be a vertical expansion joint to allow the wall to accommodate changes in temperature.
Timber expands and contracts in relation to its moisture content, causing it to crack. For example, green oak is notorious for movement when it dries out.

## Slide 14: Generating power within a building
Solar black vacuum tubes. These convert a mixture of water and antifreeze into hot water via a heat exchanger.
Notes: https://www.cse.org.uk/advice/renewable-energy/solar-hot-water

## Slide 15: Generating power within a building
Photovoltaic cells create direct current through silicone conductors built into a panel. An invertor turns this into AC at 230V.
Notes: https://www.malagasolar.eu/what-is-photovoltaics/
Tutor notes:
The PV solar cells produce direct current, the invertor is required to change it to alternating current.

## Slide 16: Generating power within a building
Heat recovery takes latent heat from exhaust air and recovers it to use on fresh air.
Notes: https://www.popularmechanics.com/home/interior-projects/how-to/a149/1275121/

## Slide 17: Generating power within a building
The previous heating methods using renewables are increasing, but gas and electric power are very commonly used for hot water, radiators and underfloor heating.
Gas boilers are slowly being phased out as the UK government drives to reduce emissions that affect global warming.
Alternative, more sustainable heating systems are being proposed to replace boilers, including ground and air source heat pumps.

## Slide 18: Heating and cooling buildings
To cool a building occupants can:
open windows to allow the movement of air
use shading to reduce solar heat gain.
To warm a building occupants can:
close windows to reduce airflow
use traditional or heat recovery systems
From a design point of view, orientating buildings so that they face south to maximise sunlight will maximise warmth.
Notes: http://hyperphysics.phy-astr.gsu.edu/hbase/work2.html

## Slide 19: Combined heat and power (CHP)
CHP is a highly efficient process that captures and utilises heat that is a by-product of the electricity generation process. It is suitable for large structures or areas where there is a need for electricity and thermal energy (eg manufacturing, commercial buildings, etc).
By generating heat and power simultaneously, CHP can reduce carbon emissions by up to 30% compared to the separate means of conventional generation via a boiler and a power station. For more information see https://youtu.be/DtA2A_3f0Os.
Notes: Combined heat and power - GOV.UK (www.gov.uk)

## Slide 20: Sustainable homes for the future
Global temperatures are forecast to rise by 1ºC on average due to global warming.
This could see the Earth experiencing greater extremes of temperature and have an impact on demand for housing that can cope with different temperature ranges.
Housing design for the future should consider the impact of climate on demand for heating and cooling/ventilation, avoiding high energy demands from heating systems and air conditioning.
In addition to innovative building design, simple measures such as painting roofs white could reduce heat build-up in cities.
Notes: See: Urban Heat: Can White Roofs Help Cool World's Warming Cities? - Yale E360

## Slide 21
Any questions?