## Slide 1: 6.3 Measurement standards, guidance and practice PowerPoint 6: Tolerances
6. Construction measurement principles

## Slide 2: Tolerances
A construction tolerance is an allowable variation in something that can be measured.
It may be:
the permitted variation from a given dimension or quantity
the range of variation permitted in maintaining a specified dimension
a permitted variation from location or alignment.
While these tolerances are a permitted deviation from perfect, the aim is always to be accurate when constructing and finishing a building.

## Slide 3: Onsite versus prefabricated processes
In the past, virtually all construction activity was performed onsite. Every element of the structure was prepared and custom fitted into the building as it was being constructed.
With more prefabricated construction being used, all component parts must be accurately made to fit together.
While a carpenter onsite can cut a beam to fit or a plumber move a radiator slightly, a window fitter with an offsite manufactured UPVC window frame that is only a few millimetres too big would not be able to fit it.

## Slide 4: Standards for tolerances
There are a numerous different standards (too many to list here) available, setting out accepted ranges of tolerance for different materials, components, construction techniques, fabrication methods, installation techniques and building types.
These range from relatively large tolerances for site layouts or landscaping to very precise tolerances for manufactured components.
It is important that tolerances are clearly specified and that they are properly understood by everyone in the construction process from the designers through to the site operatives.

## Slide 5: Tolerances: NHBC
This link to the National House Building Council (NHBC) standards website gives examples of the different tolerances allowed:
NHBC Standards 2011 (nhbccampaigns.co.uk)

## Slide 6: Worked example
The foundations of a building should measure 12m by 15m
The tolerance given is +/- 2%
The building could measure anything between
-2% = 11.76m by 14.7m
+2% = 12.24m by 15.3m
That is a variation of 0.48m by 0.6m

## Slide 7: Practical example: One World Trade Center
If a 30 storey building was leaning by 1 degree, the top would be about 1.7m out of line with the bottom.
If this was applied to the One World Trade Center in New York (shown left), how far out of line would the top be?
9.5m!

## Slide 8
Any questions?