## Slide 1: PowerPoint 1: Onsite and offsite construction methods
PowerPoint presentacion
7. Building technology principles
7.1 Construction methods

## Slide 2: Construction contexts
Residential construction
Commercial construction
Industrial construction
Focuses on buildings people will live in, such as houses, apartments and housing complexes
Buildings for commercial purposes, such as offices, shops and schools
Construction of premises used for manufacturing purposes such as food processing plants and factories

## Slide 3: Traditional construction pre-1920
The construction of buildings before 1920 focused on the use of traditional methods such as:
traditional masonry materials and techniques
solid wall construction
suspended timber floors
traditional cut roofs.

## Slide 4: Onsite construction methods
Traditional onsite construction methods are still widely used in the industry. The construction phase of a project is predominantly carried out onsite with a high level of labour and resources involved. The programme of works will outline the activities that need to take place along with predicted timescales.

## Slide 5: Timber frame construction
Timber frame construction is a popular traditional building method that can be used for residential and commercial purposes. The timber frame consists of studs, rails and boarding to form a structural frame that transmits vertical and horizontal loads to the foundations.

## Slide 6: Steel frame systems
Structural steelwork has been used for many years and is still a popular choice in industry. Steel frame system(s) (SFS) are used for a variety of developments such as offices, retail units and factory units. Steel provides a high strength to weight ratio and can be adaptable in terms of moulding into shapes and sizes.
SFS consist of two key elements:
columns – upright or vertical members that carry loads down to the foundation
beams – horizontal members that transfer the loads from the floors to the columns.
This is known as a skeleton framework.

## Slide 7: Brick and block construction
Brick and block construction is a traditional method that is a key part of British architecture. Brick and block is still the most common construction method for the development of domestic dwellings in the UK. The most common form of brick and block construction is cavity walling.

## Slide 8: Container construction
In recent years there has been a rise in the use of shipping containers for construction purposes. Steel intermodal containers can be used as structural elements and adapted to create buildings. Containers are modified in a factory environment and delivered to site for assembly. There is therefore an element of offsite construction involved.

## Slide 9: Straw bale construction
Straw bale construction is a method of building that uses bales or bundles of straw.
Straw bales can be used for both structural and insulation purposes and are considered a highly sustainable building material.
Straw bales can be designed to provide load-bearing structural support to a building.

## Slide 10: Portal frames
Portal frames were first used during the Second World War and became very popular in the 1960s. They are still commonly used to create structures that require large interior spans, such as supermarkets, warehouses and agricultural buildings.
Portal frames can be made in various shapes and sizes and from a range of different primary materials including steel, concrete and timber.

## Slide 11: Construction elements

## Slide 12: Robotics
With advances in technology, robotics are increasingly being used in the construction industry. The use of robotics can address low productivity but adoption of this technology is low due to financial constraints.
Advantages | Disadvantages
Can address low productivity | Maintenance costs
Can reduce health and safety concerns | Staff upskilling and training
Reduction in human error during construction process | Technical issues and investment costs
Prevention of accidents and injuries | Changes to job roles in the sector

## Slide 13: Offsite production methods: prefabrication
Modern construction methods predominantly involve some form of prefabrication. This means that components and building elements are manufactured in a factory environment and delivered to a site, resulting in less labour-intensive and time-consuming processes. Prefabrication is becoming increasingly popular in all contexts of construction work.

## Slide 14: Advantages of prefabrication
Time – a building can be constructed and made watertight faster than traditional methods.
Quality – factory produced quality is maintained and controlled.
Waste – prefabricated systems generally produce less waste than traditional forms of construction.
Labour requirements – prefabrication systems require less skilled trades resulting in a reduction in labour costs.
Adaptability – can be used in areas where traditional methods are not feasible.

## Slide 15: Modular construction
Modular buildings are prefabricated units that consist of repeated elements known as modules. Standardised components are produced in a factory environment and delivered to the site for installation.
Modular systems are becoming increasingly popular as suitable building materials become more widely available. There is more control over quality in a factory environment. Modular buildings can provide longevity and sustainability.

## Slide 16: Precast structures
Precast concrete structures are produced by casting concrete in moulds that are left to cure in a controlled environment, usually a factory setting. Precast concrete is typically used for structural elements such as walls, floors and stairs. Precasting can be very effective when repeated elements are required.

## Slide 17: Preconstructed panels
Preconstructed panels are mass produced offsite. This is another alternative to traditional site-based methods. Elements can include doors, windows and floors, or even whole walls. Panels can be made from a variety of different materials including timber, steel, concrete and masonry.

## Slide 18: 3-D printing
3-D printing was first developed and trialled in the 1980s. At the early stages it was extremely expensive and it was also difficult to rectify errors. In modern construction, 3-D printing is becoming increasingly popular due to better technology and understanding. Such printing can involve a 3-D printer attached to an arm that builds onsite, or more commonly, 3-D printers are used in a factory environment to print elements to be delivered to the site and installed at a later stage.

## Slide 19: Maintenance
Building maintenance is the process of ensuring a building retains both its aesthetics and its function.
Lack of maintenance can result in decay, degradation and reduced performance. Maintenance may be to the fabric of the building or in the form of upgrades.

## Slide 20: Building defects

## Slide 21: Maintenance
Maintenance can be anything from painting exterior windows and doors to structural changes. The building owner will generally be responsible for financing maintenance activities but the contractor who constructed the building may have an initial responsibility for problems that occur early in the life of the building.

## Slide 22
The maintenance cycle

## Slide 23: Renovations
Cosmetic renovations focus on aesthetics and are ‘surface upgrades’ that can often give a new lease of life to a building. Examples include painting, replacing flooring or updating fixtures and fittings.
Cosmetic renovations
Structural renovations are more extensive and focus on the structural aspects of the building, such as removing, changing or adding any load-bearing elements.
Structural renovations

## Slide 24: Refurbishment
When buildings exceed their lifespan they may need to be refurbished. This allows the useful life of a building to be extended. Old technologies can be removed and replaced by updated systems and materials. This can bring a new lease of life to a dilapidated building.
Refurbishment can often be a less costly and more sustainable option than redevelopment.

## Slide 25: Refurbishment
When buildings are reaching the end of their useful life they can often become a financial burden. The building will incur high maintenance costs to keep it operational and functional as many parts will need updating and replacing as they break down.
Refurbishment process
A condition survey will be carried out and the new designs agreed with the client. The building is stripped of any elements due to be replaced. Any harmful or hazardous elements such as asbestos are removed by specialist personnel. The new design is constructed and service upgrades or adaptions are installed.
The building is commissioned and handed over to the client.

## Slide 26
Any questions?