## Slide 1: PowerPoint 1: Principles of magnetism and electromagnetism
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
explain the basic principles of magnetism and electromagnetism including
  flux density
  magnetic strength
  conductors and insulators
  Fleming’s rules.

## Slide 3: Key abbreviations and symbols throughout the sessions
The sessions that make up Electrical and electronic principles make frequent use of key abbreviations and symbols. Make a note of them now:
alternating current (AC)
ampere (A)
angular frequency (ω)
capacitive reactance (XC)
coulomb (C)
current (I)
direct current (DC)
electromotive force (emf)
farad (F)
flux density (B)
hertz (Hz)
impedance (Z)

## Slide 4: Key abbreviations and symbols throughout the sessions
inductance (unit: Henry) (L)
inductive reactance (XL)
joule (J)
magnetic field strength (H)
magnetomotive force (mmf)
metre (m)
microfarad (uF)
microsiemens (μS)
milliampere (mA)
millisecond (ms)
ohm (Ω)
phi (magnetic flux) (φ)
resistance (R)
second (s)
siemens (S)
tesla (T)
time constant of circuit Ꞇ (tau)
volt (V)
watt (W)
weber (Wb)

## Slide 5: What is magnetism?
The molecules (collection of atoms) of most ferrous (iron) metals are naturally each a magnet with a north- and south-seeking pole. The spinning electrons form a tiny magnet and the direction of this spin produces the direction of a magnetic field.

## Slide 6: Magnetic fields
A magnetic field can be conceptualised from the above drawing which shows lines of force or magnetic flux associated with a bar magnet. The arrows indicate the direction of the magnetic field flowing from north to south, outside the magnet.
The lines of magnetic flux will not cross and will show a tendency to always take the shortest possible route between opposing poles within the confines of the field pattern.

## Slide 7: Flux and flux density
The magnetic flux is usually designated with the symbol φ (phi) measured in webers (Wb). The number of lines of flux passing through a given area (A) is called the flux density (B) and its units are webers/m2 or teslas (T).
So that:
B = φ / A
φ
A

## Slide 8
Electricity and magnetism are two closely related subjects. Electricity is produced with the aid of a magnetic field and an electric current can produce a magnetic field.
An electromagnetic force can be produced by flowing current through a coil of wire (mmf – magnetomotive force).
The greater the electric current supplied to a coil of wire of a certain length the greater the magnetic field strength (H) whose units are ampere (A) turns per metre (m).
H =
Where:
I = current, N = the number of turns of the coil of wire, L = inductance.
Magnetic field strength or intensity

## Slide 9
By plotting the relationship between B (flux density) and H (magnetic field strength), you can see, for a given current, the flux density of different materials.
B and H relationship
This helps manufacturers of electrical machinery to choose the best materials for different applications such as motors and transformers.

## Slide 10: What is electricity?
Electricity is concerned with the movement of electrons. An electric current can be explained as an interchange of electrons between neighbouring atoms. To produce such an interchange requires a form of energy.

## Slide 11: Atomic structure
Every atom has a nucleus which contains positive electrical charges called protons and neutral charges called neutrons. Orbiting around the nucleus is an equal number of negatively charged electrons.
Hydrogen has 1 proton in its nucleus and 1 electron in orbit.
Copper has 29 protons in its nucleus and 29 electron in orbit.
Aluminum has 13 protons in its nucleus and 13 electron in orbit.

## Slide 12: Free electrons
In some substances, including most of the common metals, it is possible to cause electrons to break away from their atoms. Electrons that can be easily separated from their atoms are called free electrons.
If an atom loses an electron, it becomes positively charged. It is therefore able to attract an electron from another atom.

## Slide 13
Substances which have free electrons are known as conductors. Conversely, those atoms from which electrons cannot break away, or at least find it very difficult, are called insulators.
If we now take a conductor with its atomic structure of free electrons and put it in an electric circuit under electrical pressure, we can see a moving picture of current flow. The free electrons move in the direction of the current.
Conductors, insulators and current flow

## Slide 14: Typical electrical units
+
-
V
I
R
Voltage sources can be batteries or generators. The unit of voltage is the volt (V).
Current (I) – current is the flow of electricity in a closed circuit. Its units are amps (A).
Resistance is the resistance to current in a circuit. Less resistance = more current for a fixed voltage. Its units are the ohm (Ω).

## Slide 15: Electromagnetism
Consider the diagram below. X shows current flowing into the screen and the dot shows current flowing out of the screen with the resultant flux in the direction shown.
Copper wire
Flux
If you place this current-carrying conductor in a magnetic field a force is exerted on the conductor. The direction of force is determined by Fleming’s left-hand rule.

## Slide 16
Current going into the screen.
Field going from north to south.
Creates a force moving the conductor to the right.
This is the basis of an electric motor operation.
Fleming’s left-hand rule

## Slide 17
If a wire is wrapped around an iron core and a current applied, the direction of the resultant field can be determined from the right-hand grip rule.
Thumb points in the direction of the field.
Fingers point in the direction of current.
Right-hand grip rule

## Slide 18: Electromagnetic induction
In 1821, Michael Faraday showed that if a conductor moves in a magnetic field an electromotive force (emf) is produced in that conductor. The emf only lasts while the movement takes place.
Faraday’s laws
An induced emf is established in a circuit whenever the magnetic field linking that circuit is changed.
The magnitude of an emf induced in a circuit is proportional to the rate of change of the magnetic flux linking that circuit.

## Slide 19: Fleming’s right-hand rule
N
S
Motion
The conductor is forcibly moved through the field in the direction shown.
This produces an emf in the direction shown. This is the basis of generator operation.
Conductor

## Slide 20: Induction motors
Induction motors are an example of a moving flux crossing the rotor conductors and producing a force which causes the rotor to turn.
(Fleming’s left-hand rule).
Rotor
Supply
Moving flux in motor coils

## Slide 21: Generators
Generators are an example of forcibly moving conductors using an external machine (prime mover) through a field to produce an emf
(Fleming’s right-hand rule).
Generator
Prime mover

## Slide 22: Transformers
Transformers have two coils, with the supply voltage connected to the primary coil.
This produces a moving (alternating) flux which cuts across the secondary coils. This produces an emf in the secondary coils.
Transformers are used to change the level of voltage. Such transformers are called step up or step down transformers.

## Slide 23
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.