## Slide 1: PowerPoint 7: Protection systems, waveforms and signals
PowerPoint presentation
8. Electrical and electronic principles
8.1 Principles of electrical and electronic systems

## Slide 2: Objectives
By the end of this session learners should be able to:
explain the importance of protection systems
demonstrate an understanding of different waveforms and signals in electrical and electronic systems.

## Slide 3: Protection systems
Protection systems are essential in electrical and electronic applications for the following reasons:
to isolate faulty circuits
to prevent electric shock
to provide good isolation for maintenance
to prevent damage to equipment.

## Slide 4: Prospective fault current
Protection
Protection equipment should be capable of isolating prospective fault current under fault conditions to prevent explosion or risk of fire.
Consider a 440V supply and a cable length of the resistance shown.
G
Load
0.025Ω
0.01Ω
Prospective fault current
S/C fault
S/C Fault
I = = 17600A
I = = 12571A
The protection equipment must be able to isolate those potentially high currents.

## Slide 5: Voltage and current transformers
In large power systems, voltages and currents can be high when operating normally. In fault conditions, prospective current values can be many times more than the normal operating current. Protection systems have to be able to safely measure these large voltages and currents. To do this, voltage and current transformers are used.
Transformers are typically made up of two windings – a primary and a secondary – which are completely electrically isolated from each other. They connect through the magnetic flux created.
In this way, they can proportionally reduce the voltage and current to more manageable levels.

## Slide 6: Transformer protection systems
The diagram shows normal operating values of 440V and 300A.
However, the secondary voltage and currents are 110V and 5A.
If the primary values increase, then the secondary values increase proportionally. The protection relays can react to this increase.

## Slide 7: Distance relay protection
Znormal
Distance relay
V
I
Zfault
Znormal =
Zfault
When a fault occurs, the voltage tends to reduce and the current increases. When Znormal > Zfault the distance relay trips. The distance to the fault can also be determined.

## Slide 8: Inverse time overcurrent relays
In this type of relay, operating time is inversely changed with current. So, high currents will operate the overcurrent relay faster than low currents.
Current
Time
I1
I2
t2
t1
At I1 trip time t1
at I2 trip time t2
t2 < t1
Normal current

## Slide 9: Residual current devices (RCDs)
Residual current devices (RCDs) operate using a special type of transformer which can measure the difference in current between two conductors.
Typically, these are the live conductor and the neutral conductor in a domestic circuit.
If there is a small difference between the supply and the return current – for example, if you accidently touch the live conductor – then the device will trip the circuit.
RCDs should operate with small difference currents, for example, 30mA in milliseconds (ms).

## Slide 10: Protecting against lightning
During thunderstorms, the potential of the cloud is raised significantly higher than the ground potential and the surrounding air loses its insulating property.
For lightning to occur, the resistance of the air must be overcome – if this happens then a huge discharge occurs in the form of a lightning strike.
Lightning strikes can cause untold damage to power lines and their associated electrical equipment, so some form of protection is required.

## Slide 11: Lightning arrestors
Lightning arrestors protect electrical equipment from high voltage surges caused by lightning strikes. They can be installed at the top of transmission poles. They consist of a spark gap and a series non-linear resistors connected to earth.
The spark gap is set so that the operating voltage of the transmission line will not overcome the air gap. However when a high voltage occurs the air gap is overcome and a spark crosses the gap.
The high voltage across the non-linear resistors causes the resistance value to be low, so that the current surge flows to earth.
Transmission line
Air gap
Non-linear resistor
Earth

## Slide 12: Waveforms and signals
The most common waveform in electrical distribution is the sine wave. A sine wave is represented by one frequency. Different types of waveform can be generated depending on the application – for example, generating sounds in music – as these waveforms are made up of multiple frequencies generating different sounds. Examples are shown below.
Triangular wave
Square wave
Sawtooth wave
Rectangular wave

## Slide 13: Analogue signals
An analogue signal is one type of continuous time-varying signal.
A sine wave is one type of analogue signal. All analogue signals can be defined by using amplitude, time period and frequency.
An analogue signal can represent process variables such as temperature, pressure and flow. Analogue signals can be AC or DC. One of the problems with analogue signals is they can be distorted: hence, the information they carry can be corrupted.
Example of an analogue signal

## Slide 14: Digital signals
A digital signal represents data as a sequence of discrete values.
In most digital circuits, the signal is represented by having two possible values. This is called a binary signal or logic signal.
The signals are represented by two voltage values, typically one near a reference value 0V and the other at another reference value, which has commonly been set at 5V.

## Slide 15: Signal conditioning
The variables of temperature and pressure (for example) have analogue values but different units. This would require a multi-input measuring system that could interpret both types of signal. However, through signal conditioning we can convert these signals to have the same type of analogue signal which represents their individual values.
0 to 20 bar
0 to 3000C
Pressure to current converter
P/I
Temperature (uV) to current converter
V/I
0 bar 0mA
20 bar 10mA
0 to 10mA
0oC 0mA
300oC 10mA
0 to 10mA
0 to 10mA

## Slide 16: Further conditioning
If the analogue signal of 0 to 10mA is to be analysed by a computer, then we have to carry out further conditioning by using an analogue to digital (A/D) converter. We then get a binary representation of the varying analogue value.
0 to 10mA input
4 bit A/D converter
0
0
0
0
to
1
1
1
1

## Slide 17: Signal processing
Once the information has been converted into a digital signal, signal processing takes place. It feeds the digitised information back for use in the real world. It does this in one of two ways – either digitally or in an analogue format by going through a digital to analogue (D/A) converter. All of this occurs at very high speeds.
300oC
1
1
1
1
D/A converter
10mA

## Slide 18: Logic gates
A logic gate is a series of transistors connected together to give one or more outputs, each output being based on the input or combination of inputs supplied to it.
Types of logic gates include AND, OR or NOT.

## Slide 19
Fan in and fan out
Millions of logic gates are required in a computer system to process the signals and convert them into real, recognisable data.
One important factor is how many inputs can be designed for a single gate (fan in) and the maximum number of logic inputs that a single output can drive (fan out).
Logic gates
Logic gates
Input
Storage register
Storage register
Output

## Slide 20
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.