## Slide 1: PowerPoint 2: Electrical and electronic components
PowerPoint presentation
9. Mechatronics
9.1 The key components of a mechatronics system

## Slide 2: Objectives
By the end of this session learners should be able to:
describe the electrical/electronic components of a mechatronics system, including:
  sensors
  transducers
  actuators.
Infrared sensor component

## Slide 3: Sensors
Commonly used sensors in mechatronic systems include:
  light dependent resistors (LDRs) (shown right) (which have a resistance that varies with the light level)
  NTC thermistors (which have a resistance that varies with the temperature level)
  proximity sensors (which detect the presence of nearby objects)
  pressure sensors (which detect changes in fluid pressure).
Sensors are used to measure changes in the environment around them. They do this by taking a signal from the environment and changing it into an electrical or electronic signal.

## Slide 4: Transducers
Commonly used transducers in mechatronic systems include:
  light, temperature, proximity, pressure and infrared sensors
  motors and solenoids
  sound outputs, such as bells, buzzers and loudspeakers.
Transducers are electrical components that convert one form of energy into another. They can be either sensors (input devices) or actuators (output devices).

## Slide 5: Actuators
Commonly used actuators in mechatronic systems include:
  AC and DC motors
  servo motors
  stepper motors
  servo motors
  solenoids.
Actuators turn an electrical, mechanical or environmental signal into a physical movement. Actuators can be active or passive, depending on whether they introduce new energy into the system or not.
M
Symbol for a motor

## Slide 6
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.