## Slide 1: PowerPoint 3: Microprocessors and microcontrollers
PowerPoint presentation
9. Mechatronics
9.1 The key components of a mechatronics system

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe some key electrical/electronic components of a mechatronics system, including the purpose and function of microprocessors and microcontrollers.
A microprocessor on a circuit board

## Slide 3: Programmable components
Microprocessors and microcontrollers are examples of programmable components. They:
  are usually in the form of an integrated circuit (IC)
  are programmed to perform different functions
  replace discrete components, such as transistors.
  You need to understand the purpose of microprocessors and microcontrollers, and how they work as part of mechatronic systems.
  What applications can you think of that might use programmable components in a mechatronic engineering context?

## Slide 4: Microprocessors
Microprocessors are processing devices widely used in computing technology.
They contain the logic and control circuitry required for a central processing unit (CPU) to perform its functions.
They receive digital data (1s and 0s), process it in line with their programming and then output the results.
In mechatronics, microprocessors are commonly used in applications such as computer-controlled robots and smart systems.

## Slide 5: Microcontrollers
Microcontrollers are small ‘computers on a chip’ with several pins or ports to connect different input and output devices.
  They use programming to replace hardware functions such as responding to sensors, latching, timing, counting and performing logic functions. This reduces the size of circuits and adds flexibility in the design of the system.
  They can be programmed using text-based, flowchart-based or block-based programming editors/languages.

## Slide 6: Peripheral interface controllers (PICs)
  A peripheral interface controller (PIC) is one of the most popular options for engineering work.
  PICs are often ‘in-circuit programmable’.
  They are available in a range of sizes, eg 8, 14, 18, 20, 28 and 40 pins.
  Most PICs have in-built analogue-to-digital signal conversion capability.

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.