## Slide 1: PowerPoint 6: Operation of PLCs
PowerPoint presentation
9. Mechatronics
9.2 The operation, function and applications of programmable logic controllers (PLCs) in mechatronic systems

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the operation of programmable logic controllers (PLCs), including sensor signal conditioning and programming.

## Slide 3: Sensor signal conditioning
Analogue signals from sensors often need to be modified, or conditioned before being transmitted to a programmable logic controller (PLC).
This is to ensure they are in a suitable format for the PLC to understand.
The simplest form of signal conditioning is converting a continuous analogue signal into a discrete digital signal (analogue to digital conversion).
Other types and methods of signal conditioning include filtering, amplification and attenuation.
1
0

## Slide 4: Programming PLCs
PLCs must be programmed using software to perform the different functions that are required of them.
Ladder logic is the most common method used for programming PLCs, but they can also be programmed using sequential function charts, function block diagrams, structured text and instruction lists.

## Slide 5: Ladder logic
Ladder logic is a programming language that uses a graphical diagram to represent a program, based on the circuit diagrams of relay logic hardware. It is mainly used for PLC software designed for industrial control applications.
Advantages and limitations of ladder logic:
  simple to use
  easy to understand and find errors
  can lack flexibility when more complex programs are required.

## Slide 6: Interpreting ladder logic

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.