## Slide 1: PowerPoint 7: Function of PLCs
PowerPoint presentation
9. Mechatronics
9.2 The operation, function and applications of programmable logic controllers (PLCs) in mechatronic systems

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the function of programmable logic controllers (PLCs), including:
  process blocks
  motor driver integrated circuits (ICs)
  interface devices.

## Slide 3: Process blocks
Programmable logic controllers (PLCs) are represented as process blocks in systems diagrams.
Process blocks respond to signals from input blocks, and use this information to control output blocks.
PLC
Signal to output block
Signal from input block
PROCESS
Notes: The layout of block diagrams is covered in more depth in topic 10, presentations 1, 2, 4 and 5.

## Slide 4: Motor driver integrated circuits
Programmable devices cannot usually provide enough current to drive motor outputs on their own.
A motor driver integrated circuit (IC) can provide this extra current boost.
One option where only simple functionality is required is a Darlington driver IC, such as the ULN2803.
One commonly used option where more complex functions are needed, such as providing bidirectional currents that allow motors to reverse, is an L293D.

## Slide 5: Interface devices
Interface devices allow communication to take place between the input and output devices, and the PLC itself.
This is important to ensure integrity and accuracy of information both sent and received.
Interface devices are usually provided in a modular design for direct connection to the PLC and ease of maintenance.
They need to be of rugged design for use in manufacturing environments, where they may be exposed to harsh conditions.

## Slide 6
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.