## Slide 1: PowerPoint 3: Assurance
PowerPoint presentation
11. Quality management
11.1 Quality standards, assurance, control and improvement

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
understand the main principles, purposes and outcomes of quality assurance
understand the difference between quality assurance and quality control
understand the main requirements of quality standards.

## Slide 3: Culture of quality
A culture of quality is defined as an environment in which everyone (managers and employees at all levels) should support and contribute to quality.
An organisation should not only follow quality guidelines, but also consistently see others taking quality-focused actions, hear others talking about quality, and feel quality all around them.
A culture of quality is based on the premise that no single tool, test or person can guarantee quality.

## Slide 4: Quality assurance (QA) and quality control (QC)
Quality assurance (QA) is about the prevention of defects and mistakes in manufactured products.
ISO 9000:2015 defines QA as: ‘part of quality management focused on providing confidence that quality requirements will be fulfilled’.
Quality control (QC) is about making sure that the product meets the accepted standard by detection.
ISO 9000:2015 defines QC as ‘Part of quality management focused on fulfilling quality requirements’.
Quality Assurance
Prevention
Quality Control
Detection
Notes: Diagram author generated

## Slide 5: QA and QC comparison
QA | QC
A managing tool | A corrective tool
Process-orientated | Product-orientated
Prevention of defects | Detection of defects
Proactive strategy | Reactive strategy
Everyone's responsibility | Testing team’s responsibility
Performed in parallel with a project | Performed after the final product has been made
Notes: Diagram author generated

## Slide 6: What is QA?
QA is all the planned and systematic activities implemented within the quality system that can be demonstrated to provide confidence that a product or service will fulfil requirements for quality.
QA is fundamentally focused on planning and documenting processes to assure quality. This includes meeting the requirements of quality, inspection and test plans.
QA is a management approach to ensure that quality standards and customer requirements are met.
Notes: Getty images: Hybrid images: 129944533

## Slide 7: QA systems
QA follows guidelines from standards and uses various systems and approaches to achieve its aim:
total quality management (TQM)
right first time
quality standards (ISO 90001 – quality management systems)
traceability
inspection and testing
document and version control.

## Slide 8: TQM
Total quality management (TQM) is the continual process of detecting, reducing or eliminating errors in manufacturing, streamlining supply chain management, improving the customer experience and ensuring that employees are up to date with training.
Do
Plan
Check
Act
Formulate objectives and processes to meet customer needs and organisational policies
Implement processes
Monitor and measure processes. Report result
Adapt, improve and change processes
TQM can be divided into four basic categories: do, plan, check, act

## Slide 9: ‘Right first time’
The concept of ensuring that any procedure is performed in the right manner the first time and every time is designed to decrease waste and increase efficiency in production.
To be successful, ‘right first time’ needs the following approach, which originates from a set of tools for process improvement called Six Sigma.
Define the problem.
Measure the problem.
Analyse the root cause.
Improve the process.
Control the process.

## Slide 10: ‘Right first time’ process
Define the problem
What is wrong with a process?
Measure the problem
What is the magnitude of the problem?
Analyse the root cause
Improve the process
Eliminate the root cause and implement process changes
Control the process
Control the process by regular reviews
What is the root cause of the problem?
The graphic below shows the ‘right first time’ process in more detail (also known as the DMAIC methodology). Notice that the first three stages focus on the problem before any changes are implemented. The final stage shows how regular reviews ensure ongoing control.

## Slide 11: Quality standards: ISO 9001
Using ISO 9001:
can increase productivity and efficiency, thus lowering the costs of an organisation, which may in turn improve profitability
can improve customer experience, resulting in repeat business, increased sales and additional income for a business
can enhance reputation, attracting new customers to an organisation.
ISO 9001 is an international standard that sets out the requirements for a quality management system. It helps businesses and organisations be more efficient and improve customer satisfaction.

## Slide 12: Your turn
Find out more about ISO 9001 by researching online.
Record three facts about the standard that you can share with the group.
How would a business or organisation benefit from it?

## Slide 13: Inspection and testing
An inspection and test plan, or inspection test plan is a document or series of documents used for quality assurance purposes.
An inspection and test plan:
outlines how the quality of a particular object will be ensured, both at its beginning and throughout its service life, or as an end product
highlights many different testing and inspection tasks – for instance, destructive testing of materials may be done during the initial phases of the project to ensure they have adequate properties.

## Slide 14: Inspection and testing
Inspection and testing involves the following.
Interpretation of specifications/ drawings.
Measurement of dimensions or other related parameters.
Selection of proper instruments/gauges.
Selection of unit(s) of measurement.
Comparison between specified and measured values. Based on the act of comparison, correct decisions can be taken.

## Slide 15: Traceability
Traceability is the ability to trace all processes from the procurement of raw materials to production and disposal, to clarify when and where the product was produced and by whom.
Traceability means full identification of: each component, batch or lot number (if appropriate); source; any documentation associated with the receipt; and any other relevant information.
As components and materials are used, the date/time, batch and product information is attached to the transaction record. If a product quality problem occurs, the manufacturer of the product must take effective measures promptly. The number of companies required to quickly recall their products due to problems has been increasing every year.
Notes: A list of product recalls can be found here: Product Recalls and Alerts - GOV.UK (www.gov.uk) Learners could be asked to choose an example and discuss the case in class.

## Slide 16: Document and version control
Quality assurance document and version control is an essential part of the quality assurance system. It is important when documents are being created, and for any records that undergo a lot of revision and redrafting. It helps to track changes and identify when key decisions were made.
It allows a business or organisation to:
approve, review and update documents
make changes and identify revision status
control document distribution
prevent use of obsolete documents
facilitate proper archiving.

## Slide 17
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.