## Slide 1: PowerPoint 10: Kanban
PowerPoint presentation
16 Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the kanban method, its benefits, limitations and implementation.

## Slide 3: What is kanban?
  Kanban (from the Japanese word kanban, meaning signboard or billboard) is a method used to manage the flow of work in a manufacturing company.
  It is a pull system, so products are only made when there is demand from customers (rather than being made as stock for a warehouse).
  It is used when the batch manufacturing of products involves several different processes or operations.

## Slide 4: Benefits of kanban
      Compared to conventional methods of controlling production, kanban normally reduces the amount of inventory, which reduces the space needed for work in progress and the money the business needs to operate.
      It reduces the time spent by operators finding the next batch of materials to work on.
      If a defect occurs in a batch it is detected quickly, which minimises scrap and the associated cost of this.
      It is easy for the operators of each process to follow.

## Slide 5: Limitations of kanban
      Scheduling each process is time consuming and can be complicated, increasing the cost of managing the activity.

## Slide 6: How is kanban implemented?
  Instructions are issued stating which batch of products must be worked on at each process.
  The instructions may be communicated by either:
        a card system
        a kanban noticeboard
        kanban ‘bins’ to hold work between processes.
  The operators must follow the kanban sequence of manufacture, making the products in the order required.

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.