## Slide 1: PowerPoint 8: SMED
PowerPoint presentation
16. Continuous improvement
16.1 Continuous improvement principles and practices

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the concept of single minute exchange of die (SMED) and how this relates to changeover times in manufacturing
outline the benefits and limitations of this approach and describe how it is carried out in practice.

## Slide 3: Changeover times in manufacturing
  During batch manufacturing, it is necessary to change processes between batches.
  This might involve swapping tools, repositioning jigs and changing machine parameters.
  During the changeover, the process is not producing products, but workers are still being paid for their activities.
  Reducing changeover times therefore has benefits for the business.

## Slide 4: What is single minute exchange of die (SMED)?
  Single minute exchange of die (SMED) is a term first used by Toyota.
  The goal of SMED is to perform every changeover between products in less than a minute.
  SMED is now commonly used to describe activities to reduce changeover times, even if the changeover takes a lot longer than a minute.

## Slide 5: Benefits of SMED
      Faster changeover between products resulting in less equipment downtime and lower manufacturing costs.
      Allows more frequent changeovers without increasing manufacturing costs, meaning batch sizes can be reduced.
      As a result a smaller inventory of finished products is needed and there is increased potential to customise batches for customers.

## Slide 6: Limitations of SMED
      Most effective in reducing changeover time when batches of products are being manufactured, with common characteristics between different products.
      May require some investment in additional tooling or jigs and fixtures.
      Time is needed to train workers in the approach and then to implement it (typically one day for each process).

## Slide 7: Activity elements during a changeover
  Internal elements are things which have to be done when the process is stopped.
        For example, sharpening the cutting tool being used.
  External elements are things that can be carried out while the process is running.
        For example, any tools needed could be located as the previous batch is being processed.

## Slide 8: How is SMED carried out?
Identify all the steps in the current changeover activity.
Remove all external elements from the changeover process.
Convert internal elements to external elements. For example, sharpening a cutting tool could be changed from an internal to an external element by having a second cutting tool, which is sharpened while the previous batch is being processed.
Standardise the process – document the most efficient new method of carrying out the changeover.
Training is essential to ensure all workers follow the improved standardised process

## Slide 9
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.